## Slide 1: REGISTER ADDRESSING:
Register addressing is the most common form of data addressing.
The MP contains the following 8-bit registers used with register addressing: AH, AL, BH, BL, CH, CL, DH, & DL.
•16-bit registers: AX, BX, CX, DX, SP, BP, SI, & DI.
It is important for instructions to use registers that are the same size.

## Slide 2: Cont.
Never Mix an 8-bit register with a 16-bit register because this is not allowed by MP & results in an error when assembled.
MOV AX, AL instruction is not allowed because these registers are of different sizes.
Exception: SHL DX, CL
None of the MOV instructions affect the flag bits.

## Slide 3: Cont.
See Table (3-1), P-78, BREY.
- A segment-to-segment register MOV instruction is about only type of register MOV instruction not allowed.
Code segment (CS) register is not normally changed by a MOV instruction, because the address of the next instruction is fund in both IP & CS. If only CS were changed, the address of the next instruction would be unpredictable. Therefore, changing CS register with a MOV instruction is not allowed.

## Slide 4: Table 3.1: register add. instructions

## Slide 5: Cont.
See fig (3.3), P-79, BREY.
MOV BX, CX
source register contents do not changed, but the destination register’s contents do changed.
The instruction moves (copies) a 1234H from register CX into register BX.
This erases the old contents (76AFH) of register BX, but the contents of CX remain unchanged.

## Slide 6: Cont.
The contents of destination register/destination memory location change for all instructions except the CMP & TEST ins.
Register array
AX BX CX
MOV BX, CX
76 | AF |  | 
 |  | 1234 | 
12 | 34 |  | 

## Slide 7: IMMEDIATE ADDRESSING:
Terms Immediate implies that the data immediately follow the hexadecimal opcode in memory.
Immediate data are constant data, while data transferred from a register are variable data.
Immediate addressing operates upon a byte/word of data.
MOV immediate instruction transfer a copy of the immediate data into a register/a memory location.

## Slide 8: Cont.
MOV AX, 3456H instruction copies 3456H from the instruction, located in the memory immediately following hexadecimal opcode into register AX.
Register array MOV AX, 3456H AX
BX
3456H
62 | 91

## Slide 9: Table 3.2:immediate addressing

## Slide 10: DIRECT DATA ADDRESSING:
Most instructions can use direct data- addressing mode.
•Two basic forms of direct data addressing:
1.Direct addressing, which applies to a MOV bet’n a memory location & AL, AX 2.Displacement addressing: applies to almost
any instruction in the instruction set.

## Slide 11: Cont.
In either case, address is formed by adding displacement to the default data segment or alternate segment address.
Direct Addressing:
  Direct addressing with a MOV instruction transfers data bet’n a memory location, located within data segment & AL (8-bit), AX (16-bit) register.

## Slide 12: Cont.
Register array Memory
AX BX CX
8AH
11235H
11234H
11233H
11232H
MOV AL, [1234H], DS = 1000H
AH | AL 8AH
8A

## Slide 13: Cont.
The effective address is formed by adding 1234H (offset address) to 1000H (data segment address of 1000H) in a system operating in real mode.
MOV instruction using this type of addressing is a 3-byte long instruction.
See table (3-3), P-82, BREY

## Slide 14: Table 3.3: Direct addressing

## Slide 15: REGISTER INDIRECT ADDRESSING:
•Register indirect addressing allows data to be addressed at any memory location through an offset address hold in any of following registers: BP, BX, DI & SI.
•Exam: BX contains 1000H & MOV AX ,[BX] executes.
•word contents of data segment offset address 1000H are copied into register AX.

## Slide 16: Cont.
•If MP operated in real mode & DS = 0100H, this instruction addresses a word stored at memory bytes 2000H & 2001H & transfer it into register AX.
Contents 2000H moved into AL &
Contents 2001H …………….AH
[] symbol denotes indirect addressing in assembly language.
see fig.(3-6), P-84, BREY

## Slide 17: Cont.
3412
AX BX CX
02002
02001
02000
CX DS
01002
01001
01000
01000
MOV AX, [BX], BX = 1000H, DS = 0100H
AH 34 | AL 12 | 
10 | 00 | 
34
12
+
1000 2000
0100

## Slide 18: Table 3.5: register indirect addressing

## Slide 19: Base-plus-Index Addressing:
Base-plus-index addressing is similar to indirect addressing because it indirectly addresses memory data.
In 8086, this type of addressing uses one base register (BP/BX) & one index register (DI/SI) to indirectly address memory.
Base register often holds the begging location of a memory array, while index register holds relative position of an element in the array.

## Slide 20: Cont.
Remember, whenever BP addresses memory data, both stack segment register & BP generate effective address.
•Locating Data with Base-plus-index Addressing:
•See Fig (3-8), P-87, BREY & Table (3-6), P-88, BREY.

## Slide 21: Fig 3.8:MOV DX, [BX + DI]
DS * 10
DS = 0100H, BX = 1000H, DI = 0010H

## Slide 23: Cont.
MOV DX, [BX + DI] or MOV DX,[BX][DI] DS = 0100H
BX = 1000H DI = 0010H
for prog. written for Intel
ASM assembler

## Slide 24
Locating array data using Base-plus-Index Addressing:
•A major use of base-plus-index addressing mode is to address elements in a memory array.
•Suppose, the elements in an array, located in data segment at memory location ARRAY,must be accessed.
•To accomplish this load BX with the beginning address of array & DI with element no. to be accessed. See fig(3-9),p-88

## Slide 25: Fig 3.9: base plus index addressing. Element (DI) of an ARRAY (BX) is addressed
ARRAY
Element
ARRAY + 5
ARRAY + 4
ARRAY + 3
ARRAY + 2
ARRAY + 1 ARRAY
BX
DI

## Slide 26: Register Relative Addressing:
Register relative addressing is similar to base-plus-index addressing & displacement addressing.
In register relative addressing, data in a segment of memory are addressed by adding displacement to the contents of a base/index register (BP, BX, DI & SI).
see fig. (3-10), P-89, BREY.

## Slide 27: Cont. Register Array
AX BX
3101H
3100H
0100H
1100H
DS * 10H
2000H 3100H
MOV AX, [BX + 1000H], BX = 0100H, DS = 0200H
A0 | 76 | 
01 | 00 | 
A076
A0
76
+
+
1000H
memory

## Slide 28: Table 3.7: register relative addressing

## Slide 29: Cont.
Displacement also can be an offset address appended to the front of [] such as:
MOV AL, DATA [DI]
Both forms of displacement also can appear simultaneously,
MOV AL DATA[DI + 3]
In all cases, both forms of displacement add to the base or base & index register within [].

## Slide 30: Base Relative-plus-Index Addressing:
The base relative-plus-index addressing mode is similar to the base-plus-index addressing mode, but it adds a displacement besides using a base register & an index register, to form the memory address.
This type of addressing mode often addresses a two dimensional array of memory data.

## Slide 31
Addressing Data with base relative-plus-index:
Base relative-plus-index addressing is least used addressing mode.
This addressing mode is too complex for frequent use in a program.
See fig(3-12),P-91, BREY
•Also see table(3-8),P-92, BREY.
MOV AX, [BX+SI+100], DS= 1000H, BX=0020H, SI=0010H, DS=1000H.

## Slide 32: Fig 3.12: base relative plus index addressing
MOV AX, [BX + SI + 100H]
DS = 1000H

## Slide 33
STACK MEMORY ADDRESSING MODES:
The stack plays an important role in all MP.
It holds data temporarily & store return addresses for procedures.
Stack memory is a LIFO (Last-in-First-out) memory, which describes the way that data are stored & removed from the stack.
data placed onto stack with a PUSH instruction & removed with a POP instruction.

## Slide 34: Cont.
CALL instruction also uses the stack to hold the return address for procedures
•RET (return) instruction to remove the return address from the stack.
The stack memory is maintained by the two register:
Stack Pointer (SP)
Stack Segment (SS)

## Slide 35: Cont.
Whenever a word of data is pushed onto the stack, the high-order 8-bits are placed in the location addressed by SP-1.
Low-order 8bits are placed in the location addressed by SP-2.
SP is then decrement by 2 so that next word of data is stored in the next available stack memory location.

## Slide 36: Cont.
SP register always points to an area of memory located within stack segment.
SP register adds to SS * 10H to form memory address in real mode.

## Slide 37
Example: PUSH BX
PUSH [BX]
=2FFE + SS*10H
=2FFE + 40000H
=42FFE
given, DS = 2000H [BX] = 0200H [SP] = 3000H [SS] = 4000H
3000H - 2 = 2FFE

## Slide 38: Cont.
PUSH BX
12 | 34
1234
12
34
+
3000
AX BX CX DX
SP
SS * 10H
42FFF
42FFE
Register Array
Memory

## Slide 39: Cont.
Whenever data Popped from the stack, low-order 8-bits are removed from the location addressed by SP.
High-order 8-bits are removed from the location addressed by SP + 1.
SP register is then incremented by 2.
PUSH & POP always store or retrieve words of data-never bytes in 8086.

## Slide 40: Cont.
12 | 34
12
34
1234
+
SS * 10H
POP CX
AX BX CX DX
SP
Register Array
Memory

## Slide 41: String Data Transfer
DI & SI –
During the execution of a string instruction, memory accesses occur through either or both of the DI and SI registers.
DI offset address accesses data in the extra segment for all string instructions.
SI offset address accesses data, by default, in the data segment.
The reason that one pointer addresses data in the extra segment and the other in the data segment is so that the MOVS instruction can move 64K bytes of data from one segment of memory to another.

## Slide 42: String Data Transfer
LODS –
The LODS instruction loads AL, AX, or EAX with data stored at the data segment offset address indexed by the SI register.
After loading AL with a byte, AX with a word, or EAX with a doubleword, the contents of SI increment, if D = 0 or decrement, if D = 1.

## Slide 43: String Data Transfer
LODS –

## Slide 44: String Data Transfer
STOS –
The STOS instruction stores AL, AX, or EAX at the extra segment memory location addressed by the DI register.
After loading AL with a byte, AX with a word, or EAX with a doubleword, the contents of DI increment, if D = 0 or decrement, if D = 1.

## Slide 45: String Data Transfer
MOVS –
One of the more useful string data transfer instructions is MOVS, because it transfers data from one memory location to another. This is the only memory-to-memory transfer allowed in the 8086–Pentium 4 microprocessors.
MOVS instruction transfers a byte, word, or doubleword from the data segment location addressed by SI to the extra segment location addressed by DI.

## Slide 46: String Data Transfer
INS – (input string)
INS instruction transfers a byte, word, or doubleword of data from an I/O device into the extra segment memory location addressed by the DI register.
The I/O address is contained in the DX register. This instruction is useful for inputting a block of data from an external I/O device directly into the memory.

## Slide 47: String Data Transfer
OUTS – (output string)
OUTS instruction transfers a byte, word, or doubleword of data from the data segment memory location address by SI to an I/O device.
The I/O device is addressed by the DX register.